## Slide 1: Fingerprint Power Button
By Luke Stodgel, Hong Zou, Yue Huang, Sheng Yu Chang

## Slide 2: Core Function
Power on PC upon providing a matching fingerprint.
We connected the fingerprint scanner to the Raspberry Pi and used python to control the scanner. When the correct fingerprint is given, the program will activate the Raspberry Pi pins and then send a signal to the PC motherboard to power it on.

## Slide 3: Motivation
There is no PC with a TouchID power button.
For security purposes, we want to control who has access to our computers.

## Slide 4: Timeline
(10/15) Began researching details about project
(11/1) Ordered parts and began designing prototype
(11/10) Began constructing prototype
(12/5) Completed prototype and made video and presentation

## Slide 5: Team Roles
We equally shared the workload.
We all wanted to understand how to build this from start to finish.

## Slide 6: Parts Used
- Old desktop computer - Wires
- Raspberry Pi - Two monitors
- Fingerprint scanner - Keyboard and mouse
- UART (Universal asynchronous receiver-transmitter) USB converter

## Slide 7: Python Scripts Used
Enroll.py
Scans and stores fingerprints
Asks you to put finger on the scanner, and it will store it
Search.py
Searches and compares your fingerprint with all stored fingerprints
If the fingerprint is matched, then the pin on the Raspberry Pi will power on the PC.

## Slide 8: Video Demo
https://www.youtube.com/watch?v=nq9HYBg0_6I&feature=youtu.be
Verbal typo at 0:53. We meant to say “3.3V output pin” instead of 5V.

## Slide 9: Challenges
Connecting fingerprint sensor to Raspberry Pi
Installing correct drivers
Figuring out how to connect the fingerprint sensor to the Raspberry Pi
Connecting sensor to UART (Universal asynchronous receiver-transmitter) USB converter
Programming in Python to get the functionality we wanted
Getting the Raspberry Pi to, after fingerprint authentication, send a command to turn on pin 11 (3.3Vout) for a few seconds before another command turns the pin off. This is so the desktop isn’t powering on and off endlessly.

## Slide 10: Challenges continued..
Figuring out the connection between the Raspberry Pi and the PC motherboard
We weren’t sure if we needed a relay or not.
We were scared of the PC or Raspberry Pi being damaged.

## Slide 11
Questions?

## Slide 12: References
Youtube tutorial
https://www.youtube.com/watch?v=4o3cGVgE2gI
Raspberry Pi Fingerprint sensor setup and function tutorial
https://tutorials-raspberrypi.com/how-to-use-raspberry-pi-fingerprint-sensor-authentication/